## Slide 1: Field-Circuit Coupled Simulation of Magnetothermal Dynamics in an HTS Solenoid
L. Bortot1,2, M. Mentink2, A. Verweij2, S. Schöps1
Special Thanks: I. Cortes Garcia, H. De Gersem, M. Maciejewski
7th International Workshop on Numerical Modelling of High Temperature Superconductors
22nd–23rd June 2021, Virtual (Nancy, France)
https://htsmod2020.sciencesconf.org/

## Slide 2: INTRODUCTION
High temperature superconductors (HTS)
Oxides (CuO2) doping with La, Y-Ga-Ba etc.
Higher critical temperature and coercive field with respect to low-temperature superconductors (LTS)
Quench
Local loss of the superconducting state
High energy-density  potentially irreversible effects!
Mitigation: artificial resistive zone increase  dilution of the Ohmic loss density
■ Copper ■ ReBCO ■ Substrate
Resistive zone
HTS tape
Figure: schematics of a copper-coated ReBCO tape
Motivation: Simulation of transient effects in circuits of accelerator magnets Field-Circuit Coupled Systems!

## Slide 3: MATHEMATICAL FORMULATION
Magnet domain decomposition
active region  Coils:
superconductors (
normal conductors
passive region  Iron yoke, air region:
normal conductors
insulators (
Field equations []
 |  | formulation in
 |  | formulation in
 |  | Heat balance equation in
 |  | Current constraint
 |  | Voltage distribution function
 |  | Current constraint
 |  | Voltage distribution function
Figure: General representation of the computational domain
[] Bortot, L., et al. "A Coupled A–H Formulation for Magneto-Thermal Transients in High-Temperature Superconducting Magnets." IEEE Transactions on Applied Superconductivity 30.5 (2020): 1-11.

## Slide 4: DISCRETE EQUATIONS
Discretization functions
Edge elements for , ( 1st and 2nd order)
Nodal elements for , (1st order)
Circuit interface
External circuit connected via electric ports
FEM model  one-port component with impedance
form | Weak form PDE module
𝐇-form | 
Coupling terms | 
Heat Balance | Heat transfer in solids
Circuit coupling | Global ODEs and DAEs
 | Weak form PDE module
𝐇-form | 
Coupling terms | 
Heat Balance | Heat transfer in solids
Circuit coupling | Global ODEs and DAEs
Linearized field-circuit coupling interface for solid conductors

## Slide 5: NUMERICAL EXAMPLE (1/2)
HTS solenoid protected by heater strips: 2D axisymmetric model and circuitry
2D FEM model
Iron core
Holder
Coil
Insulation
Heater strips
Figure: Rendering of the HTS solenoid. Part of the insulation is removed for illustration purposes.
: Homogeneous Dirichlet
Coil (normal conducting)
: Heater strips
Iron core
Holder
Figure: Domain decomposition

## Slide 6: NUMERICAL EXAMPLE (2/2)
Electrical layout
Observations: discharge the solenoid current determined by the quench
A.
B.
Coil supply loop
Heaters supply loop
0
t (ms)
5
10
150
Protection mode
A. crowbar resistance
B. Heater strips
Current discharged
Optimized Schwarz transmission condition for field-circuit coupled simulations with the waveform relaxation algorithm []
Solenoid lumped-parameter representation
() Garcia, Idoia Cortes, et al. "Optimized field/circuit coupling for the simulation of quenches in superconducting magnets." IEEE Journal on Multiscale and Multiphysics Computational Techniques 2 (2017): 97-104.

## Slide 7: (A) NUMERICAL RESULTS (1/3)
Circuital currents
Peak temperature
Current decay in the coil (left) and current discharge in the heater strips (right)
Induced quench
Adiabatic hotspot temperature in the coil, as a function of the quench detection time
Chart: Quench detection time (ms)
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
T | 168.2222 | 182.8245 | 198.5568 | 215.5101 | 233.7835 | 253.4302 | 274.6589 | 297.6125 | 322.4305 | 349.3411 | 378.5494
 | 300 | 300
Chart: Quench detection time (ms)
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
T | 168.2222 | 182.8245 | 198.5568 | 215.5101 | 233.7835 | 253.4302 | 274.6589 | 297.6125 | 322.4305 | 349.3411 | 378.5494
 | 300 | 300
Max. detection time
Time window
Chart: time (s)

## Slide 8: NUMERICAL RESULTS (2/3)
100 ms
150 ms
50 ms
20 ms
30 ms
10 ms
Temperature distribution in the superconducting coil, as a function of time
Temperature (K)
Quench
Heat diffusion
Heater strips

## Slide 9: NUMERICAL RESULTS (3/3)
Definitions, at iteration
signal (current in the magnet)
absolute & relative error
convergence error
convergence flag
Enforcement of at least three iterations per time window
Quench as abrupt change in resistivity
 High influence on the solenoid current
 More iterations needed!

## Slide 10: CONCLUSIONS AND OUTLOOK
Figure: Ohmic loss distribution in a HTS solenoid
Figure: magnetic flux density in the Feather-M2 insert dipole magnet
Figure: normalized induced current in a HTS bulk
Conclusions
A-H field formulation for HTS-based accelerator magnets
Field-circuit coupling interface based on solid conductor model
Co-simulation of HTS magnets with the waveform relaxation scheme
Outlook
Minimization of the quench detection time
Protection of HTS magnets in case of a quench
Dynamics of HTS magnets in accelerator circuits
Thank you for your attention! Contact: lorenzo.bortot@cern.ch