## Slide 1
Modelling and simulation of resistive type superconducting fault current limiter using OpenModelica.
A. DJAOUTI G. DIDIER D. NETTER and C. BONNARD
Université de lorraine, GREEN, 54500 Vandoevre-Lès-Nancy, France
abderrahmane.djaouti@univ-lorraine.fr
1. Abstract
In order to introduce high-temperature superconducting fault current limiters (SFCL) into electrical networks, a model is needed to predict the various phenomena that appear within the limiter. This paper presents a model of a resistive type superconducting fault current limiter developed in OpenModelica software. The finite difference method is used to solve the heat equation. The model considers the electrical and thermal phenomena in the thickness and the length of the HTS tape, which allows to study the presence of hot spots phenomenon. The obtained results are compared with finite element analysis.
This paper presents a multi-scale model of a rSFCL that takes into account electrical and thermal phenomena in the length and thickness of the tape (2D model).
The model is configurable and allows to simulate physical phenomena in 1D and 2D including the presence of thin layers (interfacial effects). The 3D model can be obtained by discretizing and considering a heat diffusion according to the width.
The open-source OpenModelica software offers the advantage that it is compatible with the FMI (Functional Mock-up Interface) standard for co-simulation and model exchange.
the simplicity of the finite difference method allows to reduce the calculation time of the simulation.
Conclusions & Perspectives
Power law:
The resistance of each (RE)BCO discretization element:
The final resistivity of the (RE)BCO:
The resistance of each silver and Hastelloy discretization element:
2. Electrical Model
3. Thermal Model
General heat equation:
Finite difference discretized form:
Conservation of the flux density between layers.
For the boundary conditions, the Neumann condition is applied.
The cooling:
: heat transfer coeff
𝑄𝑗: Joule losses per unit volume
𝜅: the heat conductivity
𝜌𝑚: the mass density
𝐶𝑝: the specific heat capacity
The heat flux density
Results and Comparisons
A tape of 5 mm long tape having a hot spot
( = 0.55) of 1 mm in length supplied
by a DC source equal to 100A is used.
Hot spot study in the tape length:
The solver (DASSL) integrated in OpenModelica has been used to solve the non-linear coupled equations
with a large number of variables.
Each temperature curve represents a different virtual measurement location, distributed equidistantly along
the y axis (one measurement at every 250μm)
There is excellent agreement between the models, where the curves can hardly be distinguished (<1%)
OpenModelica
Apply Kirchhoff's laws
Jc0 | Ec | n | 𝜌𝑇c | α | Rinter | 𝑇c | T0 | Width | Thickness (S Top) | Thickness (S Bottom) | Thickness (RE)BCO | Thickness (Hast)
2.5 MA cm-2 | 1 µV cm-1 | 15 | 30 µΩcm | 0.47µΩcm-1 | 40 µΩ | 90K | 77K | 4 mm | 2 µm | 2 µm | 1 µm | 50 µm
;