## Slide 1: Thermal-hydraulic models for HTS power-transmission cables: status and needs
S. Viarengo, D. Placido, L. Savoldi

## Slide 2: Outline
HTS cables for power transmissions:
  Use and design
  Materials
Models:
  1D (+1D)
  2D
  3D
Model needs
Conclusions

## Slide 3: HTS cables for power transmission
SC transmission cables (SCTC):
  Shipboard and aircraft applications (DC cables)
SC transmission lines (SCTL):
  High power AC transmission or distribution lines: TRL = 7 (*)
  DC lines: TRL = 5 (*)
(*) H. Thomas, Renew. Sust. Energ. Rev., 2016

## Slide 4: Aim of this work
Technical feasibility already demonstrated, but no long SCTL are currently in operation
Substantial cost reduction + improvement of the system safety and reliability needed to reach TRL 9
 Availability of reliable numerical models for the design, optimization and performance assessment in normal and off-normal conditions?

## Slide 5: Models: 1D (axial) - I
Only for the coolant:
[G. Angeli et al., IEEE TAS 2017]
[S. Fuchino et al., IEEE TAS 2002]
x

## Slide 6: Models: 1D (axial) - II
For the coolant and the solids:
Sinda/fluint network model
[M. Furuse et al., IEEE TAS 2011]
[Y. Sato et al., IEEE TAS 2015]
[T. Yasui et al., IEEE TAS 2017]
Simulink model, including transient coupled conduction equations for solids, and conservation laws for fluids along each pipe segment, including 2-phase and compressibility effects:
[S. Yang et al., IEEE TAS 2021]
[W. Choi et al., Energies 2020]
x
r

## Slide 7: Models: 1D (radial) and 1D + 1D (radial + axial)
[Z. Zhou et al., IEEE TAS 2013]
[G. Del-Rosario-Calaf et al., IEEE TAS 2013]
[WTB De Sousa et al., IEEE TAS 2018]
[E. Shabagin et al., Cryogenics, 2017]
[D. Kottonau et al., IEEE TAS 2019]
[WTB De Sousa et al., IEEE TAS 2019]
  ALSO COUPLED TO
  OR TO
Single phase, compressible 1D
Mass // momentum // energy conservation laws along the axis
[N. Hu et al., Physica C, 2011]
supply line
return line
return line only

## Slide 8: Models: 2D (Discrete)
Volume Element Model (VEM):
  Dimensional:
  Dimensionless:
  Coupled to FDTD electric analysis
[J.A. Souza et al., IEEE TAS 2011]
[J.C. Ordonez et al., IEEE TAS 2013]
[N.G. Suttel et al., IEEE TAS 2017]
[D. I. Doukas et al., IEEE TAS 2017]
[N.G. Suttel et al., Appl Therm Eng 2018]
[D. I. Doukas et al., IEEE TAS 2017]

## Slide 9: Models: 2D (Continuum)
2D FEM models of the SC lines
2D FD
  Coupled to global pressure drop in an open-source code
[N.G. Suttel et al., IEEE TAS 2017]
[S.J. Lee et al., Energies 2019]
Fully 2D model for solid components
Transient 1D advection in fluids
[W.T.B. De Sousa et al., Supercond. Sci. Technol. 2021]
[W.T.B. De Sousa et al., IEEE TAS 2019]
Return line only
supply line
return line

## Slide 10: Models: 3D
3D FEM thermal-hydraulic analysis on eccentric cable
3D finite element method (FEM) thermal analysis for solid core for 50 cm-long cable
[ J. He et al., IEEE TAS 2013]
[ O. Maruyama et al., IEEE TAS 2015]

## Slide 11: Needs of a general Thermal-Hydraulic model
Model features:
  Transient, 1D (axial) + 1D (lumped?) radial (different layers)
  Include V-I curve for SC materials + AC losses
  Include parasitic heat from environment (radiation)
  Flexibility to include different topological configuration
  Flexibility for different coolants ( compressible fluids, phase change)
  (include auxiliaries)
Numerics:
  Low computational cost to simulate long lengths
  Adaptive grids to capture local quenches
  Adaptive time stepping to capture different time-scales
Open-science!

## Slide 12: Conclusions
Comprehensive review of the different models currently available for thermal-hydraulic analysis of HTS SCTL / SCTC has been presented
Based on the experience gained in fusion SC cables/magnets modelling, the needs of a general thermal-hydraulic model have been highlighted
Open-source should become the standard!